Oxygen & Airway Management Practical

Candidate:

Evaluator:

| Skill | Possible Points | Earned Points |  |
| --- | --- | --- | --- |

Suction

| Initiates universal precautions | 1 |  | CPI |
| --- | --- | --- | --- |
| Properly assembles suction device and inspects for leaks | 1 |  |  |
| Opens patient’s mouth using the cross finger technique and inserts the catheter appropriately | 1 |  |  |
| Applies suction in a side to side or circular motion as the catheter is withdrawn (no longer than 15 seconds) | 1 |  | CPI |

Oropharyngeal and Nasopharyngeal Airways

| Selects the proper size OPA | 1 |  |  |
| --- | --- | --- | --- |
| Opens patient’s mouth using the cross finger technique and properly inserts OPA | 1 |  | CPI |
| Selects the proper size NPA and lubricates it | 1 |  |  |
| Properly inserts the NPA | 1 |  | CPI |

Oxygen Administration

| Inspects tank, regulator, and O ring for damage or leaks | 1 |  |  |
| --- | --- | --- | --- |
| Leaks tank to clear dirt or debris | 1 |  |  |
| Correctly assembles regulator and turns on O2 | 1 |  | CPI |
| Selects nasal cannula and connects to regulator, sets flow to 4-6 L/min, and properly positions device on patient | 2 |  | CPI |
| Selects non-rebreather (NRB) and connects to regulator, sets flow to 12-15 L/min, inflates bag, and properly positions device on patient | 2 |  | CPI |
| Selects bag valve mask (BVM) and connects to regulator, sets flow to 15 L/min, maintains open airway and mask seal | 2 |  | CPI |
| Demonstrates adequate ventilation (rate and depth) on the mannequin | 1 |  |  |
| Removes all devices from patient, turns off oxygen flow, bleeds regulator device to “0”, and places tank on side | 2 |  |  |

| TOTAL | 20 | ___/20 |  |
| --- | --- | --- | --- |

PASS		FAIL

Quality Points

| Efficiency | 2 |  |  |
| --- | --- | --- | --- |
| Confidence | 2 |  |  |
| Additional Medical Knowledge | 2 |  |  |

| TOTAL | 26 | ___/26 |  |
| --- | --- | --- | --- |

Skill Quality Assurance – Middlebury Patrol Additional Evaluation (Select one of three options and initial)

| EXCEPTIONAL - This candidate appears ready to go out on a call today with knowledge and confidence demonstrated in this practical. |  |
| --- | --- |
| SUFFICIENT - This candidate has a grasp on material, and is on track. |  |
| TEXTBOOK – This candidate has done nothing to show evaluators that they have any understanding of how this practical translates into a real world scenario. This candidate appears to have only memorized practical evaluation sheet. |  |